## Slide 1: STM32 Dist.
Micro104

## Slide 2: Analog peripherals
DAC (4.1)
  DAC wave generation lab (4.1.1)
ADC (4.2)
  ADC Poll lab (4.2.1)
  ADC Interrupt lab (4.2.2)
  ADC DMA lab (4.2.3)
4

## Slide 3: 4.1.1 DAC wave generator lab

## Slide 4: Use DAC as wave generator
Objective
  Learn how to setup DAC as wave generator in CubeMX
  How to Generate Code in CubeMX and use HAL functions
Goal
  Configure DAC as wave generator in CubeMX and Generate Code
  Learn how start it in project
4.1.1

## Slide 5: Use DAC as wave generator
Create project in CubeMX
  Menu > File > New Project
  Select STM32F4 > STM32F429/439 > LQFP144 > STM32F439ZITx
CubeMX DAC selection
  Select DAC OUT2
4.1.1

## Slide 6: Use DAC as wave generator
CubeMX DAC configuration
  TAB>Configuration>Analog>DAC>Parametr Settings
  Enable Output buffer
  Button OK
4.1.1

## Slide 7: Use DAC as wave generator
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can Generate Code
  Menu > Project > Generate Code
4.1.1

## Slide 8: Use DAC as wave generator
Start process DAC generation (same for DMA, ADC)
  Non blocking start process
Peripheral Initializations
Start Process
HAL_DAC_Start
Set value
HAL_DAC_SetValue
4.1.1

## Slide 9: Use DAC as wave generator
Open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 2 */ and /* USER CODE END 2 */ tags
  and /* USER CODE BEGIN 3 */ and /* USER CODE END 3 */ tags
For DAC start use function
  HAL_DAC_Start(DAC_HandleTypeDef* hdac, uint32_t Channel)
DAC set DAC value
  HAL_DAC_SetValue(DAC_HandleTypeDef* hdac, uint32_t Channel, uint32_t Alignment, uint32_t Data)
4.1.1

## Slide 10: CubeMX and OpenSTM32

## Slide 11: Open new Nucleo project
Open SW4STM32 (System workbench for STM32)
Select the workspace path
I select location of my project generated by CubeMX
But it depends on personal preference and Eclipse knowledge

## Slide 12: Eclipse start
Close the welcome panel
Then the Project explorer and code browser window will be maximized

## Slide 13: Eclipse Import project 1
Menu>File>Import…
Select Existing Project into Workspace
Next

## Slide 14: Eclipse Import project 2
Use Select root directory
Browse for directory position
In my case I search for GPIO_Test directory
IDE warns us that directory is already in workspace (ignore)
Next

## Slide 15: Use DAC as wave generator
Solution
  DAC setup and start
  Create the wave
/* USER CODE BEGIN 2 */
HAL_DAC_Start(&hdac,DAC_CHANNEL_2);
/* USER CODE END 2 */
/* USER CODE BEGIN 3 */
/* Infinite loop */
while (1)
{
HAL_DAC_SetValue(&hdac, DAC_CHANNEL_2, DAC_ALIGN_12B_R, value_dac);
value_dac++;
if(value_dac>4095)
{
value_dac=0;
}
HAL_Delay(1);
}
/* USER CODE END 3 */
4.1.1

## Slide 16: Eclipse Modify project
Now CubeMX project is in our workspace
/* Infinite loop */
/* USER CODE BEGIN WHILE */
while (1)
{
/* USER CODE END WHILE */
/* USER CODE BEGIN 3 */
while (1)
{
HAL_DAC_SetValue(&hdac, DAC_CHANNEL_2, DAC_ALIGN_12B_R, value_dac);
value_dac++;
if(value_dac>4095)
{
value_dac=0;
}
HAL_Delay(1); }
/* USER CODE END 3 */
/* USER CODE BEGIN 2 */
HAL_DAC_Start(&hdac,DAC_CHANNEL_2);
/* USER CODE END 2 */

## Slide 17: Eclipse project configuration
Right click on Project>Properties or ALT+ENTER

## Slide 18: Eclipse project settings
In “C/C++ Build”
You can find “Settings”
Here is settings of your project like in Keil (includes, optimization and others)

## Slide 19: Eclipse debug configuration 1
Go to “Run/Debug settings”
Click “New…”

## Slide 20: Eclipse debug configuration 2
Select “Ac6 STM32 Debugging”
Press “OK” Button

## Slide 21: Eclipse debug configuration 3
Select Debbuger tab
Select Use local script
Search for *.cfg script
Usual path is
XXX\Ac6\SystemWorkbench \plugins \fr.ac6.mcu.debug_1.0.0.xxxxxxxxx \resources\openocd\scripts\st_board
Click on “Apply” and “OK”

## Slide 22: Eclipse debug configuration 4
Click on “Apply” and “OK”

## Slide 23: Eclipse Run debug
Menu Run>Debug As> Ac6 STM32 C/C++ Application

## Slide 24: Eclipse Run debug
The compilation starts
If everything is OK, IDE offers you to switch to Debug perspective
Click “Yes” (possibly check “Remember my decision” before)

## Slide 25: Eclipse Run debug
Enjoy debug!

## Slide 26: Eclipse Run debug
To leave debug
Click red square
Change back perspective to editor

## Slide 27: Eclipse debug for different board
If you want to debug different board you must create own *.cfg file
It is important to change the ST-Link type
And the work size
# This is an ST NUCLEO F401RE board with a single STM32F401RET6 chip.
# http://www.st.com/web/catalog/tools/FM116/SC959/SS1532/LN1847/PF260000
source [find interface/stlink-v2-1.cfg]
set WORKAREASIZE 0x10000
source [find target/stm32f4x_stlink.cfg]
# use hardware reset, connect under reset
reset_config srst_only srst_nogate

## Slide 28: 4.2.1 ADC Poll lab

## Slide 29: Use ADC in polling mode
Objective
  Use the DAC part from previous lab
  Learn how to setup ADC in CubeMX
  How to Generate Code in CubeMX and use HAL functions
Goal
  Configure ADC in poll in CubeMX and Generate Code
  Learn how to start ADC and measure the DAC
  Verify the measured wave in STMStudio (http://www.st.com/web/en/catalog/tools/PF251373 require JAVA)
4.2.1

## Slide 30: Use ADC in polling mode
Create project in CubeMX
  Menu > File > New Project
  Select STM32F4 > STM32F429/439 > LQFP144 > STM32F439ZITx
CubeMX DAC selection
  Select DAC OUT2
  Select ADC IN13
4.2.1

## Slide 31: Use ADC in polling mode
Hardware connection
  Connect DAC out2 PA5 and ADC1 IN13 PC3 together
4.2.1

## Slide 32: Use ADC in polling mode
CubeMX ADC configuration
  TAB>Configuration>Analog>ADC1>Parametr Settings
  Set ADC1
  Set sampling time for CH13
  Button OK
DAC from previous example
4.2.1

## Slide 33: Use ADC in polling mode
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can Generate Code
  Menu > Project > Generate Code
4.2.1

## Slide 34: Use ADC in polling mode
Start process ADC(same for DMA, DAC, TIM)
  Non blocking start process
Peripheral Initializations
Start Process
HAL_DAC_Start
Peripheral Initializations
Start Process
HAL_DAC_Start
4.2.1

## Slide 35: Use ADC in polling mode
Open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 2 */ and /* USER CODE END 2 */ tags
  and /* USER CODE BEGIN 3 */ and /* USER CODE END 3 */ tags
For DAC start use function
  HAL_DAC_Start(DAC_HandleTypeDef* hdac, uint32_t Channel)
  HAL_ADC_PollForConversion(ADC_HandleTypeDef* hadc, uint32_t Timeout)
  HAL_ADC_GetValue(ADC_HandleTypeDef* hadc)
DAC functions
  HAL_DAC_Start(DAC_HandleTypeDef* hdac, uint32_t Channel)
  HAL_DAC_SetValue(DAC_HandleTypeDef* hdac, uint32_t Channel, uint32_t Alignment, uint32_t Data)
4.2.1

## Slide 36: Use ADC in polling mode
Solution
  Variables
  DAC setup and start
/* USER CODE BEGIN 2 */
HAL_DAC_Start(&hdac,DAC_CHANNEL_2);
HAL_DAC_SetValue(&hdac, DAC_CHANNEL_2, DAC_ALIGN_12B_R, value_dac);
/* USER CODE END 2 */
/* USER CODE BEGIN PV */
uint32_t value_adc;
uint32_t value_dac=0;
/* USER CODE END PV */
4.2.1

## Slide 37: Use ADC in polling mode
Solution
  Main loop with DAC set and ADC set
/* USER CODE BEGIN 3 */
/* Infinite loop */
while (1)
{
HAL_ADC_Start(&hadc1);
HAL_ADC_PollForConversion(&hadc1,10);
value_adc=HAL_ADC_GetValue(&hadc1);
HAL_DAC_SetValue(&hdac, DAC_CHANNEL_2, DAC_ALIGN_12B_R, value_dac);
value_dac++;
if(value_dac>4095){
value_dac=0;
}
HAL_Delay(1);
}
/* USER CODE END 3 */
4.2.1

## Slide 38: Use ADC in polling mode
Test the functionality
  We need the address of variable value_adc
  This can be found usually in debug mode in watch, my address is 0x2000005C (depends on compilator and optimizations)
Start the STMStudio
  Set the ST Link SWD
  Right click into Display variable settings
  Select NEW
4.2.1

## Slide 39: Use ADC in polling mode
STM studio settings
  Set value_adc address my 0x2000005C
  Set 16bit unsigned val
  Right click on this line
  Select Send To VarViewer1
4.2.1

## Slide 40: Use ADC in polling mode
STM studio settings
  Viewers settings is on bottom
  Set the correct upper value to 4096(12bit)
4.2.1

## Slide 41: Use ADC in polling mode
STM studio settings
  Now press green play button
  And you will see content of value_adc
4.2.1

## Slide 42: 4.2.2 ADC Interrupt lab

## Slide 43: Use ADC with interrupt
Objective
  Use the DAC part from previous lab
  Learn how to setup ADC with interrupt in CubeMX
  How to Generate Code in CubeMX and use HAL functions
Goal
  Configure ADC in interrupt in CubeMX and Generate Code
  Learn how to start ADC and measure the DAC
  Verify the measured wave in STMStudio (http://www.st.com/web/en/catalog/tools/PF251373 require JAVA)
4.2.2

## Slide 44: Use ADC with interrupt
Create project in CubeMX
  Menu > File > New Project
  Select STM32F4 > STM32F429/439 > LQFP144 > STM32F439ZITx
CubeMX DAC selection
  Select DAC OUT2
  Select ADC IN13
4.2.2

## Slide 45: Use ADC with interrupt
CubeMX ADC configuration
  TAB>Configuration>Analog>ADC1>Parametr Settings
  Set ADC1
  Set sampling time for CH13
  Button OK
DAC from previous example
4.2.2

## Slide 46: Use ADC with interrupt
CubeMX ADC configuration
  TAB>NVIC settings
  Enable ADC1 interrupt
  Button OK
4.2.2

## Slide 47: Use ADC with interrupt
CubeMX NVIC configuration
  Because we want use the Systick for delay in interrupt The ADC interrupt priority must be changed
  TAB>Configuration>System>NVIC
  Change ADC1 preemption priority to 1
4.2.2

## Slide 48: Use ADC with interrupt
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can Generate Code
  Menu > Project > Generate Code
4.2.2

## Slide 49: Use ADC with interrupt
HAL Library ADC with IT flow
Start process with interrupt generation at end of process
HAL_ADC_Start_IT
ADCInitializations
including peripheral interrupt NVIC initializations
HAL_ADC_IRQHandler
process callback
HAL_ADC_ConvCpltCallback
process Error callback
HAL_ADC_ErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
ADC_IRQHandler
4.2.2

## Slide 50: Use ADC with interrupt
Open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 2 */ and /* USER CODE END 2 */ tags
  and /* USER CODE BEGIN 4 */ and /* USER CODE END 4 */ tags
For DAC start use function
  HAL_ADC_Start_IT(ADC_HandleTypeDef* hadc, uint32_t Channel)
  HAL_ADC_GetValue(ADC_HandleTypeDef* hadc)
ADC complete callback function
  HAL_ADC_ConvCpltCallback(ADC_HandleTypeDef* hadc)
DAC functions
  HAL_DAC_Start(DAC_HandleTypeDef* hdac, uint32_t Channel)
  HAL_DAC_SetValue(DAC_HandleTypeDef* hdac, uint32_t Channel, uint32_t Alignment, uint32_t Data)
4.2.2

## Slide 51: Use ADC with interrupt
Solution
  Variables
  DAC setup and start ADC/DAC
/* USER CODE BEGIN 2 */
HAL_DAC_Start(&hdac,DAC_CHANNEL_2);
HAL_DAC_SetValue(&hdac, DAC_CHANNEL_2, DAC_ALIGN_12B_R, value_dac);
HAL_ADC_Start_IT(&hadc1);
/* USER CODE END 2 */
/* USER CODE BEGIN PV */
uint32_t value_adc;
uint32_t value_dac=0;
/* USER CODE END PV */
4.2.2

## Slide 52: Use ADC with interrupt
Solution
  ADC complete callback routine
/* USER CODE BEGIN 4 */
void HAL_ADC_ConvCpltCallback(ADC_HandleTypeDef* hadc)
{
value_adc=HAL_ADC_GetValue(&hadc1);
HAL_DAC_SetValue(&hdac, DAC_CHANNEL_2, DAC_ALIGN_12B_R, value_dac);
value_dac++;
if(value_dac>4095){
value_dac=0;
}
HAL_Delay(1);
HAL_ADC_Start_IT(&hadc1);
}
/* USER CODE END 4 */
4.2.2

## Slide 53: Use ADC with interrupt
STM studio settings
  Check functionality again with STMstudio
4.2.2

## Slide 54: 4.2.3 ADC with DMA lab

## Slide 55: Use ADC with DMA
Objective
  Use the DAC part from previous lab
  Learn how to setup ADC with DMA in CubeMX
  How to Generate Code in CubeMX and use HAL functions
Goal
  Configure ADC in DMA in CubeMX and Generate Code
  Learn how to start ADC and measure the DAC
  Verify the measured wave in STMStudio (http://www.st.com/web/en/catalog/tools/PF251373 require JAVA)
4.2.3

## Slide 56: Use ADC with DMA
Create project in CubeMX
  Menu > File > New Project
  Select STM32F4 > STM32F429/439 > LQFP144 > STM32F439ZITx
CubeMX DAC selection
  Select DAC OUT2
  Select ADC IN13
4.2.3

## Slide 57: Use ADC with DMA
CubeMX ADC configuration
  TAB>Configuration>Analog>ADC1>Parameter Settings
  Set ADC1
  Set sampling time for CH13
  DMA Continuous requests
  Button OK
DAC from previous example
4.2.3

## Slide 58: Use ADC with DMA
CubeMX ADC configuration
  TAB>DMA Settings
  Button ADD
  DMA request ADC1
  Peripheral to memory direction
  Circular mode
  Memory increment
  Half word data width
  Button OK
4.2.3

## Slide 59: Use ADC with DMA
Now we set the project details for generation
  Menu > Project > Project Settings
  Set the project name
  Project location
  Type of toolchain
Now we can Generate Code
  Menu > Project > Generate Code
4.2.3

## Slide 60: Use ADC with DMA
HAL Library ADC with DMA flow
Start process with interrupt generation at end of process
HAL_ADC_Start_DMA
ADCInitializations
including peripheral interrupt NVIC initializations
HAL_DMA_IRQHandler
process callback
HAL_ADC_ConvCpltCallback
process Error callback
HAL_ADC_ErrorCallback
HAL_ERROR
HAL_OK
HAL_BUSY
DMA1_StreamX_IRQHandler
4.2.3

## Slide 61: Use ADC with DMA
Open the project in our IDE
  The functions we want to put into main.c
  Between /* USER CODE BEGIN 2 */ and /* USER CODE END 2 */ tags
  and /* USER CODE BEGIN 3 */ and /* USER CODE END 3 */ tags
For DAC start use function
  HAL_ADC_Start_DMA(ADC_HandleTypeDef* hadc, uint32_t* pData, uint32_t Length)
DAC functions
  HAL_DAC_Start(DAC_HandleTypeDef* hdac, uint32_t Channel)
  HAL_DAC_SetValue(DAC_HandleTypeDef* hdac, uint32_t Channel, uint32_t Alignment, uint32_t Data)
4.2.3

## Slide 62: Use ADC with DMA
Solution
  Variables
  DAC setup and start ADC/DAC
/* USER CODE BEGIN 2 */
HAL_DAC_Start(&hdac,DAC_CHANNEL_2);
HAL_DAC_SetValue(&hdac, DAC_CHANNEL_2, DAC_ALIGN_12B_R, value_dac);
HAL_ADC_Start_DMA(&hadc1,(uint32_t*)&value_adc,1);
/* USER CODE END 2 */
/* USER CODE BEGIN PV */
uint32_t value_adc;
uint32_t value_dac=0;
/* USER CODE END PV */
4.2.3

## Slide 63: Use ADC with DMA
Solution
  ADC main routine
/* USER CODE BEGIN 3 */
/* Infinite loop */
while (1)
{
HAL_DAC_SetValue(&hdac, DAC_CHANNEL_2, DAC_ALIGN_12B_R, value_dac);
value_dac++;
if(value_dac>4095){
value_dac=0;
}
HAL_Delay(5);
HAL_ADC_Start(&hadc1);
HAL_Delay(5);
}
/* USER CODE END 3 */
4.2.3

## Slide 64: Use ADC with DMA
STM studio settings
  Check functionality again with STMstudio
4.2.3

## Slide 65: www.st.com/stm32